Design Document
KAT ADC Test Gateware

Introduction

The KAT ADC Test gateware is a simple design which allows 128KB of data from any two KAT ADC channels to be captured and retrieved.

KAT ADC Test Register Map

Name	Addr	Size	Function
CTRL	0x1000000	0x4	A positive edge on bit 0 of this 32-bit register will start an ADC capture. Bits 9:8 and 13:12 control the ADC channel source for QDR0 and QDR1 respectively. The source is decoded as follow: 0 – ADC0 I, 1 – ADC0 Q, 2 – ADC1 – I, 3 – ADC 1 - Q
STATUS	0x1000100	0x4	When least significant bit of this register is set the ADC is busy with a capture
OVERRANGE	0x1000200	0x4	When bits 0:1 are set these indicates an out-of-range condition for ADC0 channel I OR Q. / When bits 9:8 are set these indicates an out-of-range condition for ADC1 channel I OR Q
SYNC_COUNT0	0x1000300	0x4	This value indication the number of pulses received from the sync input on ADC 0
SYNC_COUNT1	0x1000400	0x4	This value indication the number of pulses received from the sync input on ADC 1
ADC_CTRL	0x20000	0x10	This register provides control functions for both KAT ADCs. See OPB KAT ADC Controller register map below for detailed behaviour.
IIC_ADC0	0x40000	0x10	This maps a KAT IIC Controller to access the IIC on ADC0. See below for further details on IIC access.
IIC_ADC1	0x48000	0x10	This maps a KAT IIC Controller to access the IIC on ADC1. See below for further details on IIC access.
QDR0	0x2000000	0xFFFFFF	This memory contains the data from a capture, the source of which depends on the CTRL source setting.
QDR1	0x3000000	0xFFFFFF	This memory contains the data from a capture, the source of which depends on the CTRL source setting.
BOARD_ID	0x0	0x2	This should always contain 0xdeaf

OPB KAT ADC Controller Register Map

Name	Offset	Length	Function
DCMCTRL	0x1	0x1	Bit 1 controls the direction of the clock to data phase adjustment of ADC0; writing 1 to bit 0 will adjust the clock phase by one increment / Bit 5 controls the direction of the clock to data phase adjustment of ADC1; writing 1 to bit 4 will adjust the clock phase by one increment
RESET	0x3	0x1	Writing '1' to bit 0 resets ADC0; writing '1' to bit 1 resets ADC1
ADC0_DATA	0x4	0x2	Sets the data word for the three wire interface (ADC0)
ADC0_ADDR	0x6	0x1	Sets the address for the three wire interface (ADC0)
ADC0_START	0x7	0x1	Writing '1' to bit 0 will start a three-wire interface configuration word load (ADC0)
ADC1_DATA	0x8	0x2	Sets the data word for the three wire interface (ADC1)
ADC1_ADDR	0xa	0x1	Sets the address for the three wire interface (ADC1)
ADC1_START	0xb	0x1	Writing '1' to bit 0 will start a three-wire interface configuration word load (ADC1)

KAT IIC Controller Register Map

Name	Offset	Length	Function
OPFIFO	0x2	0x2	Setting Bit 10 will terminate the IIC byte access with a STOP Sequence and send a “No Acknowledge” with on the associated read. / Setting Bit 9 will initiate the IIC byte access with a START Sequence. / When bit 8 is high the byte transfer is a read, when low a write. / Bits 7:0 contain the data to be written and are unused in the write case / This FIFO will latch on a LSByte write.
RXFIFO	0x6	0x2	Bits 7:0 of this FIFO contains the data read during a byte read transfer. / This FIFO will latch on a LSByte read.
STATUS	0xb	0x1	Bit[0] RXFIFO empty flag / Bit[1] RXFIFO full flag / Bit[2] RXFIFO overflow error latch / Bit[4] OPFIFO empty flag / Bit[5] OPFIFO full flag / Bit[6] OPFIFO overflow error latch / Bit[8] NACK on write error latch / Any write to these register will clear all latches and reset all fifos

KAT IIC Notes

OPFIFO and RXFIFO are 32 deep.

KAT ADC / KAT IIC Examples (From UBoot)

Note: when entering Uboot commands ensure operations are entered all at once otherwise iic device will timeout

To Access Local (Ambient) Temperature on TMP421 (IIC ADDR 0x4C, REGISTER ADDR 0x0)

mw d0040000 298; # START, WRITE, DATA=0x98 (4C << 1 + 0x0(IIC WRITE))
mw d0040000 000; # WRITE, DATA=0x00 (Register Address)
mw d0040000 299; # START(REPEATED), WRITE, DATA=0x99 (4C << 1 + 0x1(IIC READ))
mw d0040000 500; # STOP, READ
md d0040004 1; # Read Data from RXFIFO

mw d0040000 298; mw d0040000 000; mw d0040000 299; mw d0040000 500; md d0040004 1;

To Access ADC Temperature on TMP421 (IIC ADDR 0x4C, REGISTER ADDR 0x1)

mw d0040000 298; # START, WRITE, DATA=0x98 (4C << 1 + 0x0(IIC WRITE))
mw d0040000 001; # WRITE, DATA=0x01 (Register Address)
mw d0040000 299; # START(REPEATED), WRITE, DATA=0x99 (4C << 1 + 0x1(IIC READ))
mw d0040000 500; # STOP, READ
md d0040004 1; # Read Data from RXFIFO

mw d0040000 298; mw d0040000 001; mw d0040000 299; mw d0040000 500; md d0040004 1;

To Write EEPROM DATA (IIC ADDR 0x51, ADDR 0x4, DATA 0xDEADBEEF)

mw d0040000 2A2; # START, WRITE, DATA=0xA2 (0x51 << 1 + 0x0(IIC WRITE))
mw d0040000 004; # WRITE, DATA=0x04 (Register Address)
mw d0040000 0de; # WRITE, DATA=0xde
mw d0040000 0ad; # WRITE, DATA=0xad
mw d0040000 0be; # WRITE, DATA=0xbe
mw d0040000 4ef; # WRITE, DATA=0xef

mw d0040000 2A2; mw d0040000 004; mw d0040000 0de; mw d0040000 0ad; mw d0040000 0be; mw d0040000 4ef;

To READ EEPROM DATA (IIC ADDR 0x51, ADDR 0x4)

mw d0040000 2A2; # START, WRITE, DATA=0xA2 (0x51 << 1 + 0x0(IIC WRITE))
mw d0040000 004; # WRITE, DATA=0x04 (Register Address)
mw d0040000 2A3; # START(REP), WRITE, DATA=0xA2 (0x51 << 1 + 0x1(IIC READ))
mw d0040000 100; # READ
mw d0040000 100; # READ
mw d0040000 100; # READ
mw d0040000 500; # STOP, READ
md d0040004 1;
md d0040004 1;
md d0040004 1;
md d0040004 1;

To SET ADC1 PCA9555 Output 0 [7:0] to enabled (IIC ADDR 0x21, ADDR 0x6)

mw d0040000 242; # START, WRITE, DATA=0x42 (21 << 1 + 0x0(IIC WRITE))
mw d0040000 006; # WRITE, DATA=0x06 (Register Address)
mw d0040000 400; # STOP, WRITE, DATA=0x00 (OE_n [7:0] = 0x0)

To SET ADC1 PCA9555 Output 0 [7:0] (IIC ADDR 0x21, ADDR 0x2, Data 0xF0)

mw d0040000 242; # START, WRITE, DATA=0x42 (21 << 1 + 0x0(IIC WRITE))
mw d0040000 002; # WRITE, DATA=0x02 (Register Address)
mw d0040000 4F0; # STOP, WRITE, DATA=0xF0